/******************************************************************************\
 * enable this section if you have TMC26X motor drivers.
 * you need to import the TMC26XStepper library into the Arduino IDE for this
 ******************************************************************************/

// @section tmc

//#define HAVE_TMCDRIVER
#if ENABLED(HAVE_TMCDRIVER)

  //#define X_IS_TMC
  //#define X2_IS_TMC
  //#define Y_IS_TMC
  //#define Y2_IS_TMC
  //#define Z_IS_TMC
  //#define Z2_IS_TMC
  //#define E0_IS_TMC
  //#define E1_IS_TMC
  //#define E2_IS_TMC
  //#define E3_IS_TMC

  #define X_MAX_CURRENT 1000 // in mA
  #define X_SENSE_RESISTOR 91 // in mOhms
  #define X_MICROSTEPS 16 // number of microsteps

  #define X2_MAX_CURRENT 1000
  #define X2_SENSE_RESISTOR 91
  #define X2_MICROSTEPS 16

  #define Y_MAX_CURRENT 1000
  #define Y_SENSE_RESISTOR 91
  #define Y_MICROSTEPS 16

  #define Y2_MAX_CURRENT 1000
  #define Y2_SENSE_RESISTOR 91
  #define Y2_MICROSTEPS 16

  #define Z_MAX_CURRENT 1000
  #define Z_SENSE_RESISTOR 91
  #define Z_MICROSTEPS 16

  #define Z2_MAX_CURRENT 1000
  #define Z2_SENSE_RESISTOR 91
  #define Z2_MICROSTEPS 16

  #define E0_MAX_CURRENT 1000
  #define E0_SENSE_RESISTOR 91
  #define E0_MICROSTEPS 16

  #define E1_MAX_CURRENT 1000
  #define E1_SENSE_RESISTOR 91
  #define E1_MICROSTEPS 16

  #define E2_MAX_CURRENT 1000
  #define E2_SENSE_RESISTOR 91
  #define E2_MICROSTEPS 16

  #define E3_MAX_CURRENT 1000
  #define E3_SENSE_RESISTOR 91
  #define E3_MICROSTEPS 16

#endif

// @section TMC2130

/**
 * Enable this for SilentStepStick Trinamic TMC2130 SPI-configurable stepper drivers.
 *
 * To use TMC2130 drivers in SPI mode, you'll also need the TMC2130 Arduino library
 * (https://github.com/makertum/Trinamic_TMC2130).
 *
 * To use TMC2130 stepper drivers in SPI mode connect your SPI2130 pins to
 * the hardware SPI interface on your board and define the required CS pins
 * in your `pins_MYBOARD.h` file. (e.g., RAMPS 1.4 uses AUX3 pins `X_CS_PIN 53`, `Y_CS_PIN 49`, etc.).
 */

//#define HAVE_TMC2130DRIVER

#if ENABLED(HAVE_TMC2130DRIVER)

  //#define TMC2130_ADVANCED_CONFIGURATION

  // CHOOSE YOUR MOTORS HERE, THIS IS MANDATORY
  //#define X_IS_TMC2130
  //#define X2_IS_TMC2130
  //#define Y_IS_TMC2130
  //#define Y2_IS_TMC2130
  //#define Z_IS_TMC2130
  //#define Z2_IS_TMC2130
  //#define E0_IS_TMC2130
  //#define E1_IS_TMC2130
  //#define E2_IS_TMC2130
  //#define E3_IS_TMC2130

  #if ENABLED(TMC2130_ADVANCED_CONFIGURATION)

    // If you've enabled TMC2130_ADVANCED_CONFIGURATION, define global settings below.
    // Enabled settings will be automatically applied to all axes specified above.
    //
    // Please read the TMC2130 datasheet:
    // http://www.trinamic.com/_articles/products/integrated-circuits/tmc2130/_datasheet/TMC2130_datasheet.pdf
    // All settings here have the same (sometimes cryptic) names as in the datasheet.
    //
    // The following, uncommented settings are only suggestion.

    /* GENERAL CONFIGURATION */

    //#define GLOBAL_EN_PWM_MODE 0
    #define GLOBAL_I_SCALE_ANALOG 1 // [0,1] 0: Normal, 1: AIN
    //#define GLOBAL_INTERNAL_RSENSE 0 // [0,1] 0: Normal, 1: Internal
    #define GLOBAL_EN_PWM_MODE 0 // [0,1] 0: Normal, 1: stealthChop with velocity threshold
    //#define GLOBAL_ENC_COMMUTATION 0 // [0,1]
    #define GLOBAL_SHAFT 0 // [0,1] 0: normal, 1: invert
    //#define GLOBAL_DIAG0_ERROR 0 // [0,1]
    //#define GLOBAL_DIAG0_OTPW 0 // [0,1]
    //#define GLOBAL_DIAG0_STALL 0 // [0,1]
    //#define GLOBAL_DIAG1_STALL 0 // [0,1]
    //#define GLOBAL_DIAG1_INDEX 0 // [0,1]
    //#define GLOBAL_DIAG1_ONSTATE 0 // [0,1]
    //#define GLOBAL_DIAG1_ONSTATE 0 // [0,1]
    //#define GLOBAL_DIAG0_INT_PUSHPULL 0 // [0,1]
    //#define GLOBAL_DIAG1_INT_PUSHPULL 0 // [0,1]
    //#define GLOBAL_SMALL_HYSTERESIS 0 // [0,1]
    //#define GLOBAL_STOP_ENABLE 0 // [0,1]
    //#define GLOBAL_DIRECT_MODE 0 // [0,1]

    /* VELOCITY-DEPENDENT DRIVE FEATURES */

    #define GLOBAL_IHOLD 22 // [0-31] 0: min, 31: max
    #define GLOBAL_IRUN 31 // [0-31] 0: min, 31: max
    #define GLOBAL_IHOLDDELAY 15 // [0-15] 0: min, 15: about 4 seconds
    //#define GLOBAL_TPOWERDOWN 0 // [0-255] 0: min, 255: about 4 seconds
    //#define GLOBAL_TPWMTHRS 0 // [0-1048576] e.g. 20 corresponds with 2000 steps/s
    //#define GLOBAL_TCOOLTHRS 0 // [0-1048576] e.g. 20 corresponds with 2000 steps/s
    #define GLOBAL_THIGH 10 // [0-1048576] e.g. 20 corresponds with 2000 steps/s

    /* SPI MODE CONFIGURATION */

    //#define GLOBAL_XDIRECT 0

    /* DCSTEP MINIMUM VELOCITY */

    //#define GLOBAL_VDCMIN 0

    /* MOTOR DRIVER CONFIGURATION*/

    //#define GLOBAL_DEDGE 0
    //#define GLOBAL_DISS2G 0
    #define GLOBAL_INTPOL 1 // 0: off 1: 256 microstep interpolation
    #define GLOBAL_MRES 16 // number of microsteps
    #define GLOBAL_SYNC 1 // [0-15]
    #define GLOBAL_VHIGHCHM 1 // [0,1] 0: normal, 1: high velocity stepper mode
    #define GLOBAL_VHIGHFS 0 // [0,1] 0: normal, 1: switch to full steps for high velocities
    // #define GLOBAL_VSENSE 0 // [0,1] 0: normal, 1: high sensitivity (not recommended)
    #define GLOBAL_TBL 1 // 0-3: set comparator blank time to 16, 24, 36 or 54 clocks, 1 or 2 is recommended
    #define GLOBAL_CHM 0 // [0,1] 0: spreadCycle, 1: Constant off time with fast decay time.
    //#define GLOBAL_RNDTF 0
    //#define GLOBAL_DISFDCC 0
    //#define GLOBAL_FD 0
    //#define GLOBAL_HEND 0
    //#define GLOBAL_HSTRT 0
    #define GLOBAL_TOFF 10 // 0: driver disable, 1: use only with TBL>2, 2-15: off time setting during slow decay phase

    //#define GLOBAL_SFILT 0
    //#define GLOBAL_SGT 0
    //#define GLOBAL_SEIMIN 0
    //#define GLOBAL_SEDN 0
    //#define GLOBAL_SEMAX 0
    //#define GLOBAL_SEUP 0
    //#define GLOBAL_SEMIN 0

    //#define GLOBAL_DC_TIME 0
    //#define GLOBAL_DC_SG 0

    //#define GLOBAL_FREEWHEEL 0
    //#define GLOBAL_PWM_SYMMETRIC 0
    //#define GLOBAL_PWM_AUTOSCALE 0
    //#define GLOBAL_PWM_FREQ 0
    //#define GLOBAL_PWM_GRAD 0
    //#define GLOBAL_PWM_AMPL 0

    //#define GLOBAL_ENCM_CTRL 0

  #else

    #define X_IHOLD 31 // [0-31] 0: min, 31: max
    #define X_IRUN 31 // [0-31] 0: min, 31: max
    #define X_IHOLDDELAY 15 // [0-15] 0: min, 15: about 4 seconds
    #define X_I_SCALE_ANALOG 1 // 0: Normal, 1: AIN
    #define X_MRES 16 // number of microsteps
    #define X_TBL 1 // 0-3: set comparator blank time to 16, 24, 36 or 54 clocks, 1 or 2 is recommended
    #define X_TOFF 8 // 0: driver disable, 1: use only with TBL>2, 2-15: off time setting during slow decay phase

    #define X2_IHOLD 31
    #define X2_IRUN 31
    #define X2_IHOLDDELAY 15
    #define X2_I_SCALE_ANALOG 1
    #define X2_MRES 16
    #define X2_TBL 1
    #define X2_TOFF 8

    #define Y_IHOLD 31
    #define Y_IRUN 31
    #define Y_IHOLDDELAY 15
    #define Y_I_SCALE_ANALOG 1
    #define Y_MRES 16
    #define Y_TBL 1
    #define Y_TOFF 8

    #define Y2_IHOLD 31
    #define Y2_IRUN 31
    #define Y2_IHOLDDELAY 15
    #define Y2_I_SCALE_ANALOG 1
    #define Y2_MRES 16
    #define Y2_TBL 1
    #define Y2_TOFF 8

    #define Z_IHOLD 31
    #define Z_IRUN 31
    #define Z_IHOLDDELAY 15
    #define Z_I_SCALE_ANALOG 1
    #define Z_MRES 16
    #define Z_TBL 1
    #define Z_TOFF 8

    #define Z2_IHOLD 31
    #define Z2_IRUN 31
    #define Z2_IHOLDDELAY 15
    #define Z2_I_SCALE_ANALOG 1
    #define Z2_MRES 16
    #define Z2_TBL 1
    #define Z2_TOFF 8

    #define E0_IHOLD 31
    #define E0_IRUN 31
    #define E0_IHOLDDELAY 15
    #define E0_I_SCALE_ANALOG 1
    #define E0_MRES 16
    #define E0_TBL 1
    #define E0_TOFF 8

    #define E1_IHOLD 31
    #define E1_IRUN 31
    #define E1_IHOLDDELAY 15
    #define E1_I_SCALE_ANALOG 1
    #define E1_MRES 16
    #define E1_TBL 1
    #define E1_TOFF 8

    #define E2_IHOLD 31
    #define E2_IRUN 31
    #define E2_IHOLDDELAY 15
    #define E2_I_SCALE_ANALOG 1
    #define E2_MRES 16
    #define E2_TBL 1
    #define E2_TOFF 8

    #define E3_IHOLD 31
    #define E3_IRUN 31
    #define E3_IHOLDDELAY 15
    #define E3_I_SCALE_ANALOG 1
    #define E3_MRES 16
    #define E3_TBL 1
    #define E3_TOFF 8

  #endif // TMC2130_ADVANCED_CONFIGURATION

#endif // HAVE_TMC2130DRIVER