LCD Menu's Changes.

Description:			Allows more Custom Menus to be added.

Marlin Version: 		1.1

Sketch:  			ultralcd.h

Line:  				 656

Additional Information): 	Inserted below -  MENU_ITEM(gcode, MSG_AUTO_HOME, PSTR("G28"));

Or find a menu or submenu to place required new menu items.

Code added:

MENU_ITEM(gcode, "Auto Home X/Y", PSTR("G28 X0 Y0"));

MENU_ITEM(gcode, "Auto Home Z", PSTR("G28 Z0"));

MENU_ITEM(gcode, "Lower Heatbed", PSTR("G1 Z200

MENU_ITEM(gcode, "Pause Print", PSTR("M600"));

MENU_ITEM(gcode, "Resume Print", PSTR("M24  MENU_ITEM(gcode, "Turn On H/B Fan", PSTR("M42 P4     S255"));   MENU_ITEM(gcode, "Turn Off H/B Fan", PSTR("M42 P4 S0"));

M119 Gcode changes

Marlin Version: 		1.1 Developement

Description:			M119 is used to report status of endstop switches. It can be edited to

report additional swiches like the filament present switch.

Sketch:  			Marlin_main.cpp

Line:  				 3887

Additional Information):

Code added:

#if HAS_FILRUNOUT

SERIAL_PROTOCOLPGM(MSG_FILAMENT);                                                                        SERIAL_PROTOCOLLN(((READ(FILRUNOUT_PIN)^FIL_RUNOUT_INVERTING)?MSG_FILRUNOUT:MSG_FILRUNIN));

#endif

Also

Sketch:  			language.h

Line:  				145

Code added:

#define MSG_FILAMENT            "Filament: "

#define MSG_FILRUNOUT          "Out "

#define MSG_FILRUNIN              "Present “

Also

Sketch:  			language_en.h

Description:			If using another language will need to be added to it.

Line:  				 24

Code added:

#ifndef MSG_FILAMENT

#define MSG_FILAMENT          "Filament: "

#endif

#ifndef MSG_FILRUNOUT

#define MSG_FILRUNOUT        "Out "

#endif

#ifndef MSG_FILRUNIN

#define MSG_FILRUNIN            "Present: "

#endif

-------------------------------------------------------------------------------------------------------------------------------

Filament Runout Changes.

Description:			Allows beeping when filament runs out when printing from PC.

Marlin Version: 		1.1

Sketch:  			marlin_main.cpp

Line:  				 6243

Additional Information): 	If  a   “ IS_SD_PRINTING && “ is removed from below code, an alert will be enabled

for when printing from a PC e.g. Ponterface. …

Note PC will time out after a delay as arduino isn’t able to advise why there is a delay

with not activating g-codes that were sent. . Need to check out whether pausing will

stop this time out.

Code change:

#if HAS_FILRUNOUT

if (IS_SD_PRINTING && !(READ(FILRUNOUT_PIN) ^ FIL_RUNOUT_INVERTING))  filrunout();   // Includes SD as PC can't be advised filament has runout.

#endif

Z2 Stepper motor enabling with auto sync.

Description:			Allows the use of two stepper motors (needs stepper drivers for each motor) to

control the Z axis ( print bed). Z2 Min is used for the homing of the Z2 stepper motor.

Auto syncing of both motors is used when homming the Z stepper motors.

-------------------------------------------------------------------------------------------------------------------------------------------------

Hi,

I have just upgraded my CoreXY machine to have two stepper motors for the Z axis. I wanted to be able to auto sync both of the Z stepper motors when homing.

I used my unused Extruder stepper (E2) stepper driver for the Z2 motor and added a homing switch for the Z2 motor.

I activated the Z_DUAL_STEPPER_DRIVERS,  Z_DUAL_ENDSTOPS  and assigned pin numbers for both the second Z stepper driver and Z min home sensor switch. Also added some code to Marlin.

Operation:

When the printer receives a Z home, both Z stepper motors (Z1 & Z2) drive the print platform towards the home position.

When either of the Z stepper motors min home switches are triggered the corresponding stepper motor stops.

Once both stepper motors have reached home, there is a delay before they then both move the print platform a short distance away from home and then back to home again.

Current Issue:

There appears to be a set time to home both Z stepper motors regardless of their starting positions.

This is different to normal homing of the Z axis when not using Z_DUAL_ENDSTOPS. ( No delay for small homing moves).

The set time appears to be based on the Z maximum movement setting and the homing speed.

The set time appears to be good that there is a motor drive timeout if both Z1min & Z2 min aren’t triggered.

It would be good to have some code that once both the Z1min  & Z2min are triggered that there is no time delay. This would overcome the delay with small home movements.

Apart from this issue, auto syncing of the two Z axis motors is an excellent feature of Marlin.

I had to make a few changes to the Marlin code as listed below.

--------------------------------------------------------------------------------------------------------------------------------------------------------------

Marlin Version: 		1.1

Sketch: 		       Configuration.h

Description:		        Define the Z2 homing sensor end stop pull if required.

Line 319

#define ENDSTOPPULLUP_Z2MIN

---------------------------------------------------------------------

Sketch: 	                   Configuration_adv.h

Description:		          2 lines were added for Z2min and comments added for Z2max as you don’t use both min and max for Z2

Line 148

#define Z_DUAL_STEPPER_DRIVERS                 //uncomment if using Z dual stepper drivers

#ifdef Z_DUAL_ENDSTOPS                                   //uncomment if using Z dual end stops

//#define Z2_MAX_PIN 5                                       //uncomment if using Z2MAX for homing - MAX Endstop used for Z2 axis. Define pin being used for Z2 sensor

//const bool Z2_MAX_ENDSTOP_INVERTING = true;    //uncomment if using Z2MAX for homing - true to invert- for NO switches - false for N/O switches

#define Z2_MIN_PIN 5                                          //uncomment if using Z2MIN for homing - MIN Endstop used for Z2 axis. Define pin being used for Z2 sensor

const bool Z2_MIN_ENDSTOP_INVERTING = false;     //uncomment if using Z2MIN for homing - true to invert- for NC switches - false for N/O switches

---------------------------------------------------------------------

Sketch: 		        pins_ramps13.h

Description:		         Define which pins are being used – Currently using E2 extruder driver PCB for stepper Z2 on a ramps board.

Line 48

#define Z2_STEP_PIN            36

#define Z2_DIR_PIN               34

#define Z2_ENABLE_PIN       30

---------------------------------------------------------------------

Sketch:   		        Stepper.ccp

Description:		         The following was added for Z2min

Line 933

#if HAS_Z2_MIN

SET_INPUT(Z2_MIN_PIN);

#ifdef ENDSTOPPULLUP_ZMIN

WRITE(Z2_MIN_PIN,HIGH);

#endif

#endif

---------------------------------------------------------------------

Sketch:   		          Marlin_main.cpp

Description:		          Allows M119 to report state of Z2min sensor

Line 3877

#if HAS_Z2_MIN

SERIAL_PROTOCOLPGM(MSG_Z2_MIN);

SERIAL_PROTOCOLLN(((READ(Z2_MIN_PIN)^Z2_MIN_ENDSTOP_INVERTING)?MSG_ENDSTOP_HIT:MSG_ENDSTOP_OPEN));

#endif

---------------------------------------------------------------------

Note:

Adding Z2min  to the M119 End Switch report allows a good testing all endstop sensors.

It is also very good to show how  M666 endstop adjustment works.

After a normal home you can see both Z1min and Z2min are triggered.

Give a M666 g-code with a plus or minus figure and then do a Z home and you can see how either Z1min or Z2min is trigged and the other Zmin is open.

I changed my Marlin Endstop “Open” message from ‘Open” to “ - - - “ as I think “Open” is a bit confusing as if using a switch it may in fact be closed.

Using “ Un-triggered”  is more correct but I found using ‘- - - “just looked better.

Better to have switches closed when away from home as less chance to get electrical noise that may cause a false home detect.

---------------------------------------------------------------------

Sketch:  		language.h

Description:		if using another language you may need to change that as well.

Line 155

#define MSG_ENDSTOP_OPEN                    "- - -"

---------------------------------------------------------------------