RepRap Ormerod GCode Cheat Sheet (based on dc42 firmware) 7th May 2014 v1.02

| Comm. | Parameters | Description | Example | Comment |
| --- | --- | --- | --- | --- |
| G1 | [X/Y/Z/E] | Position Feed [F] | Controlled Movement | G1 F150 X10 |
| G4 | Time in ms [P] | Dwell / Wait | G4 P500 |  |
| G10 | Pn [RS] | Set Offsets | G10 P1 S100 | Set standby(R) or Active(S) Temp (XYZ not done) |
| G20 | none | Set units to inch | G20 |  |
| G21 | none | Set units to mm | G21 |  |
| G28 | [X/Y/Z] | Home | G28 X Y |  |
| G30 | Pn [X/Y/Z] | Z Probe set at defined position | G30 P0 X60 Y20 Z0.0 |  |
| G31 | Z P | Return / set Probe at current position | G31 Z0.75 P596 | Set Z home value or return current probe value |
| G32 | none | Multiple Z Probe Auto bed compensation | G32 | M557 sets up 4 compensation points |
| G90 | none | Absolute Positioning | G90 |  |
| G91 | none | Relative Positioning | G91 |  |
| G92 | [X/Y/Z/E] Val | Set Position to value | G92 X5 Y10 |  |
| M0 | none | Stops everything after buffer is empty | M0 |  |
| M1 | none | Sleep | M1 |  |
| M18 | none | Disable all stepper motors | M18 |  |
| M20 | none | List files in gcodes folder of the SD Card | M20 |  |
| M23 | Filename | Select File for Printing | M23 print.gco |  |
| M24 | none | Start / Resume SD Card Print | M24 |  |
| M25 | none | Pause SD Card Print | M25 |  |
| M27 | none | Report SD Print status | M27 |  |
| M28 | Filename | Write program to SD Card gcodes folder | M28 print.g |  |
| M29 | Filename | Stop writing program to SD Card | M29 print.g |  |
| M80 | none | Turn on ATX Power | M80 |  |
| M81 | none | Turn off ATX Power | M81 |  |
| M82 | none | Extruder absolute positioning | M82 |  |
| M83 | none | Extruder relative positioning | M83 |  |
| M84 | none | Stop idle hold | M84 |  |
| M85 | none | Set inactive time | M85 | No action |
| M92 | XSteps_per_unit | Set steps per unit | M92 X123 |  |
| M98 | PFilename | Run macro (gcode file in sys folder) | M98 Pmacro.g |  |
| M99 | none | Return result of M98 macro | M99 |  |
| M104 | STemperature | Set extruder temperature (not waiting) | M104 S100 |  |
| M105 | none | Get extruder Temperature | M105 |  |
| M106 | Sspeed | Set Fan Speed to S and start | M106 S123 | S is value 0-255 |
| M107 | none | Turn Fan off | M107 | Deprecated. Use M106 S0 |
| M109 | S | Set Temp and wait | M109 S180 | Deprecated. Set temp and use M116 |
| M110 | Line Number[N] | Set current line number |  | (next line number = line no. +1) N123 M110 |
| M111 | SDebugLevel | Set Debug Level | M111 S0 | 0=off,1=on,2=report |
| M112 | none | Emergency Stop (Stop immediately) | M112 |  |
| M114 | none | Get Current Position | M114 | Deprecated |
| M115 | none | Get Firmware Version and Capabilities | M115 |  |
| M116 | none | Wait for ALL temperatures | M116 |  |
| M117 | none | Marlin LCD message | M117 | Does nothing treated as invalid M code |
| M120 | none | Push | M120 | Saves abs/rel, feed rate and filename |
| M121 | none | Pop | M121 | Restores values from M120 |
| M122 | none | Run Diagnostics | M122 |  |
| M126 | PTime | Open extruder valve / wait for P ms |  | No action |
| M127 | PTime | Close extruder valve / wait for P ms |  | No action |
| M135 | none | Set PID sample interval |  | No action |
| M140 | STemperature | Set heated bed temperature (not waiting) | M140 S55 |  |
| M141 | STemperature | Set chamber temperature (not waiting) | M141 S30 | Not supported |
| M190 | STemperature | Set extruder temperature and wait (like 109) | M190 S180 |  |
| M201 | [X/Y/Z] | Set maximum accelerations | M201 X800 Y800 Z5 E250 |  |
| M203 | [X/Y/Z/E] | Set maximum velocity/feed rates | M203 X12000 Y12000 Z180 E2700 |  |
| M205 | none | No action |  |  |
| M206 | [X/Y/Z] | Offset Axes | M206 X10 Y10 |  |
| M208 | [X/Y/Z] | Set maximum Axis lengths | M208 X200 Y210 Z180 |  |
| M210 | [X/Y/Z] | Set homing feed rates | M210 X1000 Y1500 |  |
| M220 | Soverride | Set Speed factor override percentage | M220 S80 |  |
| M221 | Soverride | Set Extrude factor override percentage | M221 S80 |  |
| M301 | [PIDWB] | Set hot end PID values | M300 S300 P1000 |  |
| M302 |  | Allow cold extrudes | M302 | No action |
| M304 | [PIDWB] | Set heated bed PID values |  |  |
| M305 | P[TBRLH] | Set Heater parameters | M305 P0 H40 | T(25 r), B(beta), R(SeriesR), HL( ADC high low offsets) |
| M503 | none | List config set up | M503 |  |
| M550 | PName | SetMachine name | M550 POrmerod |  |
| M551 | Ppassword | Set Web password | M55 Ppassword | Password not used by IamBurny web code |
| M552 | PIPAddr | Get/Set IP address | M552 P192.168.0.42 |  |
| M553 | PNetmask | Get/Set netmask | M553 P255.255.255.0 |  |
| M554 | PGateway | Get/Set gateway | M554 P192.168.0.1 |  |
| M555 | Pn | Emulate Firmware | M555 P2 |  |
| M556 | [S/X/Y/Z] | Set Orthogonal Axis compensation | M556 S78 X-0.65 Y0.9 Z0.2 | S=Length, X=XY, Y=YZ, Z= XZ |
| M557 | P[0,1,2,3] X Y | Set Auto compensation co-ordinates | M557 P0 X60 Y0 | Use in conjunction with G32 |
| M558 | P | Set Z probe type | M558 P1 | 1 IR, 2 Modulated IR, 3 Ultrasonic |
| M559 | Pfilename | Upload config.g | M559 Pconfig.g |  |
| M560 | Pfilename | Upload reprap.htm | M560 Preprap.htm |  |
| M561 |  | Set Identity transform | M561 | Cancels compensation |
| M562 | P | Reset temperature fault | M562 P1 | 0=bed,1=extruder. To be used with caution |
| M564 | Slimit | Enable/Disable axis limit checks | M564 S0 | 0=disable, 1=enable |
| M900 | none | Do HomeX macro | M900 |  |
| M901 | none | Do Homey macro | M901 |  |
| M906 | [X/Y/Z/E] | Set motor currents | M906 X800 Y800 Z800 E900 |  |
| M998 | P | Request resend of line | M998 P34 |  |
| M999 |  | Reset | M999 | Waits 0.5 second and resets |
| T | N | Select extruder no. (starts with 0) | T1 |  |